Episode 61 – Slope Theory

---
Episode 61 – Slope Theory
8 Different Slope Tiles:
How shall we distinguish them?

---
Position: Top vs. Bottom

---
Side: Left vs. Right

---
Height: Short vs. Tall
Tall
Tall
Short

---
How Do we Find a Point on the Slope?

---
Given:
row
y
offset
x
column
In this case:
   Slope = Δy / Δx = -0.5 Tiles / 1 Tile = -0.5
Offset = 1 Tile

---
Slopes
+0.5
-0.5

---
Offsets
Measured from the Row
0.5 Tiles
1 Tile
0 Tiles

---
General Formula:
Given:
Row
Column
Slope
Offset
One of: X or Y
row
y
offset
x
column
y – row = Slope * (x – column) + offset
 Where: column <= x <= column + 1 Tile
--------------------------------------------------
y = Slope * (x – column) + offset + row
x = (y – row – offset) / Slope + column

---
Assumptions
We are assuming we can only collide with the sloped side of the tile.

---
Use center of rectangle
Example of Y-Collision Check
y-slope
y-rect
y-slope
y-rect
center-x-rect
center-x-rect
Collision: y-rect >= y-slope
No Collision: y-rect < y-slope
Note: These checks are specific to Bottom Slopes

---
Example of X-Collision Check
y-center
y-center
x-rect
x-rect
x-slope
x-slope
Collision: x-rect <= x-slope
No Collision: x-rect > x-slope
Note: These checks are specific to Left Slopes

---
Special Considerations for
Map Collidable
- update X before we update Y
- do not check collisions with slopes in the x direction
  - This way, we move into the slope, and let updateY push us out of it in the y direction
- Check collisions with slope only in the y direction
  - Same as the last rule, just said differently
- Rule for Collision Order
  - Applies to more than just Map Collidable

---
Collision Order
- The order in which we check collision tiles
- Now that we have tiles of differing height, collision order becomes important.
  - Side Note: If we had larger delta (Game Units) collision order would already be important.

---
Collision Order: Algorithm
- If going left/right:
  - primary sort columns from left-right/right-left
  - Favor row that contains center_x
- If going up/down
  - Primary sort rows from bottom-top/top-bottom
  - Favor column that contains center_y
    - Makes it look smoother when you collide with two slopes that meet at a point

---
Collision Order: Illustrated
Going down:
Sort rows top to bottom,
Sort Columns favoring center_x
2
1
3
4

---
Special Considerations for
Walking Entities
- Walking down a slope causes “bouncing”
  - Shuffle between being on/off ground
  - We want to “stick” to slopes when we are on ground
Sticky Motion
Bouncy Motion

---
Sticky Algorithm
- For all cases: assume going down
- If we are grounded on a slope
  - If our rectangle intersects with a slope tile,
       stick to the slope
  - If we intersect with an empty space AND
    we are on a short tile AND
    the tile below is a wall,
       stick to the wall
- If we are grounded on a wall
  - If we intersect with a tall slope tile,
       stick to the slope

---
Sticky: Slope To Slope
Stick during all transitions

---
Sticky: Slope to Wall
Short Slope: Sticky Collision
Tall Slope: no sticky!
Empty
Empty
Wall
Wall
Note: Again, we stick by default if we are going up the slope.

---
Sticky: Wall to Slope
Tall Slope: Sticky
Short Slope: No sticky
Wall
Wall

---
Summary of Requirements
- A TileType to determine empty/slope/wall as well as what type of slope
  - Later it will have fluid type (air/water)
- A Collision Tile that can test collision and determine position of collision given a side (non-sticky collision)

---
Summary of Requirements
- Walking entities (so far just our player) must keep track of what TileType they are grounded on (if any)
- A way to test sticky collisions before testing non-sticky collisions